## Slide 1: Invasion of the Chinese mitten crab: development of a monitoring censor
Fonteyne Joost

## Slide 2: YOLOv3-tiny upgrades
YOLO nano
  2019
  Based on design principles from yolo family
  Outperforms YOLOv3-tiny by¹:
    8.3x smaller model size, ~17% less operations, ~10.7% higher mAP
YOLO nano underwater²
  Further simplification/improvement of YOLO nano
    Lighter and in some cases a little better than YOLO nano (underwater)
ULO & ULO Tiny²
  Enhanced YOLO nano underwater
    Adaptive pre-processing parameters (for underwater images)
    Performs only a little worse than YOLOv3 but is much smaller, performs much better than YOLOv3-tiny and YOLO nano underwater while also being smaller.
    ULO Tiny is smaller but less accurate than ULO, both outperform YOLOv3-Tiny (according to the paper)

## Slide 3: YOLOv3-Tiny upgrades
New entries in the yolo family since v3
  YOLOv4
    Also comes in a tiny version.
    More complex model requires richer training data to outperform v3
  YOLOv5 & YOLOv6
    Both controversial, made by private companies
    V4 is claimed to outperform v5
    Not much mentioning of v6
  YOLOv7¹
    July 2022
    Different flavours -> tiny version, cloud version etc
    Credited as overall best model to date²
      But not necessary better in all use cases ofc.

## Slide 4: YOLOv3-Tiny upgrades
FOMO¹
  TinyMl neural network
  Claims to work well with a fixed camera and objects of roughly the same size.
    Think conveyer beld
    Instead of bounding box for each object, only center -> OK for our application given small enough grid
    Promises high scalability, works on big GPU as well as small mcu
    Supposedly also handles tracking

## Slide 5: Raspberry pi B4 replacements
Nvidea sells dedicated processing units for edge computing
  Jetson series
    Power usage ranges from 40w to 5w. (raspberry pi B4 between 2.7 watt idle to 6.4 watt)
    A lot more expensive than raspberry pi
Maybe lighter equipment like the raspberry pi zero is possible with a lighter model.
FPGA based solutions¹
  Power consumption seems to be higher than raspberry pi B4
MCU based solution²
  With tinyMl
  Can achieve extremely small power consumption but maybe not accurate enough.
  Arduino Nicla vision with FOMO seems like a good example.
  A lot of edge ai kits are sold online

## Slide 6: Raspberry pi B4 replacements
Arduino Portenta¹
Sony Spresense¹
Arduino TinyML Kit¹
  Arduino Nano 33 BLE Sense
Himax WE-I¹
  Designed as computer vision endpoint
OpenMV¹
  Mcu camera combo for lightweight computer vision

## Slide 7: Power management
Solar power panel
  With solar power manager board
    Ex. https://www.waveshare.com/solar-power-manager.htm
    https://www.waveshare.com/product/modules/solar-panel-18v-10w.htm