## Slide 1: Invasion of the Chinese mitten crab: development of a monitoring censor
Fonteyne Joost

## Slide 2: Het probleem
De Chinese mitten krab is een invasieve soort
Zorgen voor ecologische en economische schade in vlaanderen
Ontwikkelen van een monitoring sensor
  Krabben tellen

## Slide 3: Voorgaand werk
2 college studenten voor mij (Ruben Joosen, Satish Singh)
  vission based detector en tracker
    Raspberry pi b4
    val desgin
    Geen transfer en battery support

## Slide 4: Eerste idee
Verder bouwen op bestaande vallen
  Uitwerken low tech val met tel mechanisme
Enkele problemen
  Niet verder uitgewerkt
    Niet echt een electronica/ict masterproef

## Slide 5: Verder bouwen
Verder uitbouwen punten:
  Power consumptie
    Vooral hier op focussen
  Kost
  Power supply
Onderwater wildcamera principe
Opdelen in blokken
  Power harvesting
  Bewegings detectie
  Ir led array
  Esp32

## Slide 6: Bewegings detectie
Besparen door te pollen en beweging te detecteren
  Latency van het systeem
  Uitwerken vergelijking met interne interupt timer in esp32 vs externe timer
  Uitwerken grafiek besparing met polling en bewegingdetectie
  Dfrobot microwave sensor V2
    Krabben zijn koudbloedig -> geen PIR
    Verbruik: 47mA (verwijderen indicatie leds etc)
    Interrupt pin
      Lager verbruik bij bewegings detectie en opstart -> elk pollings interval geeft sowiso winst (zonder timer in rekening te brengen)
    Onderzoeken onderwater gebruik => OK
      Toevoegen van sensitiviteit in code

## Slide 7: Ir led array
“Flash” van de camera
camera OV2640
  Standaard geen Ir
    Operatie
Donkere omgeving
Troebel water gecounterd door design
Doel? -> net genoeg licht, verbruik minimaliseren
  Max V is 2v aan 200 mA

## Slide 8: ESP32-CAM
Minder krachtig dan b4, maar verbruikt ook veel minder
Verschillende slaap functies
Beschikt over een antenne en wifi module
  Niet de focus momenteel
Nipt groot genoeg voor simpel model
  Toegegeven niet heel accuraat
    Geen 100% correcte data, wel een algemeen idee
    Iets zwaarder platform zal beter resultaat geven

## Slide 9: Model
Edge impuls
Gekozen voor FOMO (Faster objects, more objects)
  Lightweight
  Gemaakt om veel objecten van ongeveer dezelfde grote te detecteren.
    Centroids
    grid

## Slide 10: Power harvesting
Zonnepaneel
Interessante vergelijking krabben vs benodigde stroom
Lithium-Ion battery
  Gevaar -> alternatieven?
Zonnepaneel controle bord
  Stroom aanbieden van batterij (5v)
  Opladen batterij

## Slide 11: Bedankt!

## Slide 12: EXTRA slides keuze model & platform

## Slide 13: YOLOv3-tiny upgrades
YOLO nano
  2019
  Based on design principles from yolo family
  Outperforms YOLOv3-tiny by¹:
    8.3x smaller model size, ~17% less operations, ~10.7% higher mAP
YOLO nano underwater²
  Further simplification/improvement of YOLO nano
    Lighter and in some cases a little better than YOLO nano (underwater)
ULO & ULO Tiny²
  Enhanced YOLO nano underwater
    Adaptive pre-processing parameters (for underwater images)
    Performs only a little worse than YOLOv3 but is much smaller, performs much better than YOLOv3-tiny and YOLO nano underwater while also being smaller.
    ULO Tiny is smaller but less accurate than ULO, both outperform YOLOv3-Tiny (according to the paper)

## Slide 14: YOLOv3-Tiny upgrades
New entries in the yolo family since v3
  YOLOv4
    Also comes in a tiny version.
    More complex model requires richer training data to outperform v3
  YOLOv5 & YOLOv6
    Both controversial, made by private companies
    V4 is claimed to outperform v5
    Not much mentioning of v6
  YOLOv7¹
    July 2022
    Different flavours -> tiny version, cloud version etc
    Credited as overall best model to date²
      But not necessary better in all use cases ofc.

## Slide 15: YOLOv3-Tiny upgrades
FOMO¹
  TinyMl neural network
  Claims to work well with a fixed camera and objects of roughly the same size.
    Think conveyer beld
    Instead of bounding box for each object, only center -> OK for our application given small enough grid
    Promises high scalability, works on big GPU as well as small mcu
    Supposedly also handles tracking

## Slide 16: Raspberry pi B4 replacements
Nvidea sells dedicated processing units for edge computing
  Jetson series
    Power usage ranges from 40w to 5w. (raspberry pi B4 between 2.7 watt idle to 6.4 watt)
    A lot more expensive than raspberry pi
Maybe lighter equipment like the raspberry pi zero is possible with a lighter model.
FPGA based solutions¹
  Power consumption seems to be higher than raspberry pi B4
MCU based solution²
  With tinyMl
  Can achieve extremely small power consumption but maybe not accurate enough.
  Arduino Nicla vision with FOMO seems like a good example.
  A lot of edge ai kits are sold online

## Slide 17: Raspberry pi B4 replacements
Arduino Portenta¹
Sony Spresense¹
Arduino TinyML Kit¹
  Arduino Nano 33 BLE Sense
Himax WE-I¹
  Designed as computer vision endpoint
OpenMV¹
  Mcu camera combo for lightweight computer vision

## Slide 18: Power management
Solar power panel
  With solar power manager board
    Ex. https://www.waveshare.com/solar-power-manager.htm
    https://www.waveshare.com/product/modules/solar-panel-18v-10w.htm